## Slide 1: Local & Inter Networks
how are we all wired together?

## Slide 2: Computer Networks
Computer network connects two or more autonomous computers.
The computers can be geographically located anywhere.
Introduction to Computer Networks

## Slide 3: LAN, MAN & WAN
Network in small geographical Area (Room, Building or a Campus) is called LAN (Local Area Network)
Network in a City is call MAN (Metropolitan Area Network)
Network spread geographically (Country or across Globe) is called WAN (Wide Area Network)
Introduction to Computer Networks

## Slide 4: Applications of Networks
Resource Sharing
  Hardware (computing resources, disks, printers)
  Software (application software)
Information Sharing
  Easy accessibility from anywhere (files, databases)
  Search Capability (WWW)
Communication
  Email
  Message broadcast
Remote computing
Distributed processing (GRID Computing)
Introduction to Computer Networks

## Slide 5: Network Topology
The network topology defines the way in which computers, printers, and other devices are connected. A network topology describes the layout of the wire and devices as well as the paths used by data transmissions.
Introduction to Computer Networks

## Slide 6: Bus Topology
Commonly referred to as a linear bus, all the devices on a bus topology are connected by one single cable.
Introduction to Computer Networks

## Slide 7: Star & Tree Topology
The star topology is the most commonly used architecture in Ethernet LANs.
When installed, the star topology resembles spokes in a bicycle wheel.
Larger networks use the extended star topology also called tree topology. When used with network devices that filter frames or packets, like bridges, switches, and routers, this topology significantly reduces the traffic on the wires by sending packets only to the wires of the destination host.
Introduction to Computer Networks

## Slide 8: Ring Topology
A frame travels around the ring, stopping at each node. If a node wants to transmit data, it adds the data as well as the destination address to the frame.
The frame then continues around the ring until it finds the destination node, which takes the data out of the frame.
  Single ring – All the devices on the network share a single cable
  Dual ring – The dual ring topology allows data to be sent in both directions.
Introduction to Computer Networks

## Slide 9: Mesh Topology
The mesh topology connects all devices (nodes) to each other for redundancy and fault tolerance.
It is used in WANs to interconnect LANs and for mission critical networks like those used by banks and financial institutions.
Implementing the mesh topology is expensive and difficult.
Introduction to Computer Networks

## Slide 10: Network Components
Physical Media
Interconnecting Devices
Computers
Networking Software
Applications
Introduction to Computer Networks

## Slide 11: Networking Media
Networking media can be defined simply as the means by which signals (data) are sent from one computer to another (either by cable or wireless means).
Introduction to Computer Networks

## Slide 12: Networking Devices
HUB, Switches, Routers, Wireless Access Points, Modems etc.
Introduction to Computer Networks

## Slide 13: How do networks work?
another software “packetizes” the data and addresses the “envelope” to send to...
an application asks for or receives data
Software
Networks
hardware
wires
switches
ethernet
software

## Slide 14: How do networks work?
the network computer receives these packets and pushes them out the door over...
Hardware
Networks
hardware
wires
switches
ethernet
software

## Slide 15: How do networks work?
the cable connecting the computer to the network electronics
which forwards the packets to other electronics until they get to their destination
Wires & Electronics
Networks
hardware
wires
switches
ethernet
software

## Slide 16: Switches
Sw1
1.A
1.B
1.C
1.D
1.E
Sw2
2.A
2.B
2.C
if the system that is sought is not connected to that switch, the switch will send the request to other switches until it is able to find the switch that contains the sought system.
Switches work by keeping track of the systems located off their ports
System 1.A seeking System 2.B
Networks
hardware
wires
switches
ethernet
software

## Slide 17: Internal Switches
So, in Manning,
we have several switches,
several servers,
and several networks
Our switches and "main" servers for the building plug into the main switch for Manning itself.
Networks
hardware
wires
switches
ethernet
software

## Slide 18: Ethernet
In 1973, while working on a way to link Xerox’s "Alto" computer to a printer, Bob Metcalfe developed the physical method of cabling that connected devices as well as the standards that governed communication on the cable. Called Ethernet, it has since become the most popular and most widely deployed network technology in the world.
Since a signal on the Ethernet medium reaches every attached node, the destination address is critical to identify the intended recipient of the frame.
Networks
hardware
wires
switches
ethernet
software

## Slide 19: Ethernet
Most of the Ethernet ports in SILS have a speed set to 100mb
In comparison, the wireless ports are set to about 11.7 mb.
  The speed on the wireless is limited by the current available technology.
Networks
hardware
wires
switches
ethernet
software

## Slide 20: In Manning
Each wiring closet contains Tier 1 switches, to which are connected cat5 utp wires
Which themselves are connected to the main switch in the main closet
Which itself is the fiber uplink to the Tier 2 switches
The Ethernet connections go to one of several wiring closets in the building
Networks
hardware
wires
switches
ethernet
software

## Slide 21: Within Manning
Within Manning hall there are 3 networking closets to serve parts of the buildings.
Networks
hardware
wires
switches
ethernet
software

## Slide 22: Within Manning
The 3rd floor closet is in the 5th level stacks inside the library.
Networks
hardware
wires
switches
ethernet
software

## Slide 23: Within Manning
The 2nd floor closet is at the end of the hall where the faculty offices are found
Networks
hardware
wires
switches
ethernet
software

## Slide 24: Within Manning
The main closet located off the SILS Computer Lab has the fiber uplink to the campus network going into it.
This is a 1 Gbit uplink
Networks
hardware
wires
switches
ethernet
software

## Slide 25: Moving out into the star
Manning Hall
The core switches are then linked out to other Tier 2 Switches that provide links to other buildings near them.
In each building, there are switches to provide ports for each wall port.
  For each port on the wall, there is a port somewhere on a switch that it is connected to.
  for the most part, there are in fact more wall ports than switch ports, so in some cases not all the ports in a building can be connected at once.
Networks
hardware
wires
switches
ethernet
software

## Slide 26: UNC Campus
The campus is laid out in a "star" topology in which central switches are linked in a star fashion.
Different devices can be connected to a switch and a switch can include other switches, computers, wireless access points, or any other network device.
Networks
hardware
wires
switches
ethernet
software

## Slide 27: UNC Campus
A main "core" set of three (for redundancy) switches are located in the control center in Phillips
Networks
hardware
wires
switches
ethernet
software

## Slide 28: UNC Campus
- Isis uplinks to the commodity internet (the "real" internet) through Cisco Kid to MCNC(our ISP).
- We have a 2.4 Gbit uplink to the internet through this. We share a link with many of the other universities and schools in North Carolina.
- Cisco Kid is our main router that does all the "work" of finding addresses and managing traffic into, and out of our network
Cisco Kid
Networks
hardware
wires
switches
ethernet
software

## Slide 29: Manning-Loco located in the Data Center in ITS Manning
If you are accessing one of the ITS servers (like www.unc.edu or help.unc.edu) then your traffic flows through this router.
Networks
hardware
wires
switches
ethernet
software

## Slide 30: But how does it all tie together?
For the answer, we have to look at some Internet Principles

## Slide 31: The TCP/IP Standard Model
Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP
Internetworking
IP
Hardware – wires, hosts, routers
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 32: The TCP/IP Standard Model
Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP
Internetworking
IP
Hardware – wires, hosts, routers
What’s a host?
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 33: What’s a host?
Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP
Internetworking
IP
Hardware – wires, hosts, routers
What’s a host?
It’s an Internet connected computer with
an Internet address and (perhaps) a domain name.
An internet address
is a unique, 4-byte integer.
unambiguously identifies a computer (actually a network interface card)
it connects to other hosts via the next layer
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 34: The TCP/IP Standard Model
Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP
Internetworking
IP
Hardware – wires, hosts, routers
Protocols & standards are key
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 35: The Internet Evolved
Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP
Internetworking
IP
Hardware – wires, hosts, routers
Thus was born TCP/IP, which provided
Interoperability across heterogeneous machines
End-to-end communication
Reliability in the face of data link failures
Started as four machine demonstration - ARPANET (UCLA, UCSB, SRI, Utah)
But to link them into networks …
Protocols, or standards, were needed
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 36: TCP/IP????
Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP
Internetworking
IP
Hardware – wires, hosts, routers
consider the alternative
Stands for Transmission Control Protocol/Internet Protocol
Provides reliable, in-order, end-to-end transmission of data
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 37
TCP/IP????
consider the alternative
Stands for Transmission Control Protocol/Internet Protocol
Provides reliable, in-order, end-to-end transmission of data
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 38: More on Protocols
Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP
Internetworking
IP
Hardware – wires, hosts, routers
Think of sending a letter
IP makes sure the envelope is addressed in the same way so that anyone could receive it
TCP is more like sending a certified letter - you get a response that someone has received it.
TCP also makes sure that the parts of the letter are all received and are IN ORDER
protocols & standards are key
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 39: More on Protocols
Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP
Internetworking
IP
Hardware – wires, hosts, routers
Service & application layer protocols (i.e. HTTP, FTP) ensure that the sender and receiver are speaking the same language, and that the letter can be interpreted
protocols & standards are key
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 40: What are packets?
In reality, each “letter” is sent in a bunch of pieces - as if you had sent it one page at a time.
These pieces are packets.
Local Area Network
Routers
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 41: A possible piece of the Internet
Local Area Network
Routers
Let’s consider an example
Inter
networks
TCP/IP
hosts
standards
packets
examples
Could be us

## Slide 42: A possible piece of the Internet
The Internet
Local Area Network
Routers
Cisco Kid
They are there
“Ruby”
152.2.81.1
“www.bahn.de”
81.200.192.68
For us to get train tickets from “Die Bahn”, we have to send it a message
Inter
networks
TCP/IP
hosts
standards
packets
examples
Could be us

## Slide 43: A packet example
The Internet
Routers
Sally.edu
Suppose Harry wants to talk to Sally
Harry.com
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 44: A packet example
The Internet
Routers
Sally.edu
Suppose Harry wants to talk to Sally. Harry creates a message on his client
Hi, Sally, what’s up?
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 45: A packet example
The Internet
Routers
Sally.edu
His client breaks it up into small TCP packets for transmission
y, W
Hi, S
all
hat
s’ up?
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 46: A packet example
The Internet
Routers
Sally.edu
And sends it on its way
but it doesn’t have to go in a single order or along a single path
Each router reads the address and rejects it if the address isn’t on its network
Hi, S
all
hat
y, W
s’ up?
Harry.com
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 47: A packet example
The Internet
Routers
Sally.edu
Overly simplified, IP gets it to the right place, TCP puts the pieces back together in order
And so it gets to its destination
Hi, S
all
hat
y, W
s’ up?
Harry.com
Hi, Sally, what’s up?
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 48: The TCP/IP Standard Model
Or run - Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP – to provide
Internetworking
IP – to provide
Hardware – wires, hosts, routers - use
protocols & standards are key
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 49: The TCP/IP Standard Model
Or run - Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP – to provide
Internetworking
IP – to provide
Hardware – wires, hosts, routers - use
protocols & standards are key
Servers can be physical computers; Servers can also be software applications
One server (physical computer) can run many servers (software applications) at a time
So, how does the host application know when the data being received is for it?
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 50: It uses standards
Or run - Application/process to process FTP, telnet, HTTP, SSH
Transport/host to host TCP – to provide
Internetworking
IP – to provide
Hardware – wires, hosts, routers - use
protocols & standards are key
Inter
networks
TCP/IP
hosts
standards
packets
examples

## Slide 51: Next
More about the Internet